CONTROL WITH MICROCONTROLLER 
FOR PWM SINGLE-PHASE INVERTER

Laurenţiu Dimitriu, Mihai Lucanu, Cristian Aghion, Ovidiu Ursaru

“Gh. Asachi” Technical University of Iaşi,

Faculty of Electronics and Telecommunications

Bd. Carol I, no. 11,

Iaşi, 6600 Romania

ABSTRACT

The paper presents the control principle for a PWM single-phase inverter, using the capabilities of 80C552 microcontroller. The basics of control program are described. How the characteristics of the presented inverter essentially depend on the features of control system, only few microcontrollers can match the necessities for high performances. One of them is Philips 80C552. The powerful T2 timer gives its useful feature in our application.

# INTRODUCTION

The field of inverter applications requires usually a low content in harmonics of the AC voltages. One of the wide acceptance solutions consists in the PWM techniques that are moving the spectra towards high harmonics to achieve an easier filtering. The higher modulation frequency is, the smaller filters are necessary.

Using a higher modulation frequency is therefore an efficient method to improve the characteristics of PWM inverters. Unfortunately, a higher modulation frequency imposes high performances control systems. Only a reduced number of general-purpose microcontrollers could match this requirement.

Despite these contradictory aspects, the solution could be implemented using microcontroller techniques. The advantages of these techniques are too evidently to be stated.

# SOME CONTROL ASPECTS

To achieve the control system a Philips 8XC552 microcontroller was used. This one is a stand-alone high performance microcontroller designed for use in real-time application such as instrumentation, industrial control and automotive systems. The device provides in addition to the 80C51 standard functions, number of dedicated hardware functions for these applications [1], [2].

The timer T2 delivers the hardware function used in this application. Timer T2 is a 16-bit timer consisting of two registers TMH2 (HIGH byte) and TML2 (LOW byte). The 16-bit timer/counter can be switched off or clocked via a prescaler from one of two sources: fOSC / 12or an external signal. When T2 is configured as a counter, the prescaler is clocked by an external signal on T2 input. A rising edge on T2 increments the prescaler, and the maximum repetition rate is one count per machine cycle (1 MHz with 12 MHz oscillator) [2].

The timer T2 is a count-up one and is not loadable. It can be reset by the RST signal or by a rising edge on the input signal RT2, if enabled. Setting bit T2ER of TM2CON special function register enables RT2. The rising edge on RT2 also clears the prescaler.

Other useful feature of timer T2 is the compare logic. Each time timer T2 is incremented, the contents of the three compare registers CM0, CM1, and CM2 are compared with the new counter value of timer T2. When a match is found, the corresponding interrupt flag in TM2IR special function register is set at the end of the following cycle. When a match with CM0 occurs, the controller sets bits 0-5 of port 4 if the corresponding bits of the set enable register STE register are at logic 1.

When a match with CM1 occurs, the controller resets bits 0-5 of port 4 if the corresponding bits of the reset/toggle enable register RTE register are at logic 1. If RTE is "0", then P4.n is not affected by a match between CM1 or CM2 and timer T2. When a match with CM2 occurs, the controller "toggles" bits 6 and 7 if the corresponding bits of RTE are logic 1.

Eight of the nine timer T2 interrupt flags are located in special function register TM2IR. The ninth flag is TM2CON.4. The CMI0, CMI1, and CMI2 flags are set during the cycle following a match. A match will be recognized by the interrupt logic (or by polling the flags) two cycles after the match takes place.

For better characteristics, a modulation frequency of 5 KHz was used. In the Table 1 are shown the switching moments for a semiperiod of a 50 Hz single-phase PWM inverter. The corresponding pulses must be delivered by the microcontroller system. In a 10 ms time period there are 100 pulses. The values must be quantified taking into consideration the clock value of the microcontroller system. The system used has a 12 MHz crystal clock, and therefore the machine cycle is 1 microsecond. This value of 1μs is the quantified time unit of PWM control system. To be used in the control system the theoretic switching time moments are rounded considering the quantified time unit of 1 μs.

In the Table 1 both theoretical and quantified time intervals are indicated. How the symmetry axis for the semiperiod is placed at 5,000 μs, (quarter period), in the Table 1 are presented only the switches up to 5,100 μs. The switches up to 10,000 μs could be easily determined.

Table 1

| Switch state | Interval | Theoretic (μs) | Quantified (μs) | Cumulated (μs) | Moment |
| --- | --- | --- | --- | --- | --- |
| OFF | 0 - t1 | 193.94 | 193 | 193 | t1 |
| ON | t1 - t2 | 12.55 | 13 | 206 | t2 |
| OFF | t2 - t3 | 181.44 | 181 | 387 | t3 |
| ON | t3 - t4 | 25.031 | 25 | 412 | t4 |
| OFF | t4 - t5 | 168.913 | 169 | 581 | t5 |
| ON | t5 - t6 | 37.461 | 37 | 618 | t6 |
| OFF | t6 - t7 | 156.54 | 157 | 775 | t7 |
| ON | t7 - t8 | 49.721 | 50 | 825 | t8 |
| OFF | t8 - t9 | 144.412 | 144 | 969 | t9 |
| ON | t9 - t10 | 61.886 | 62 | 1031 | t10 |
| OFF | t10 - t11 | 132.3 | 132 | 1163 | t11 |
| ON | t11 - t12 | 73.765 | 74 | 1237 | t12 |
| OFF | t12 - t13 | 120.688 | 121 | 1358 | t13 |
| ON | t13 - t14 | 85.253 | 85 | 1443 | t14 |
| OFF | t14 - t15 | 109.281 | 109 | 1552 | t15 |
| ON | t15 - t16 | 96.371 | 96 | 1648 | t16 |
| OFF | t16 - t17 | 98.336 | 98 | 1746 | t17 |
| ON | t17 - t18 | 107.212 | 107 | 1853 | t18 |
| OFF | t18 - t19 | 87.646 | 88 | 1941 | t19 |
| ON | t19 - t20 | 117.321 | 117 | 2058 | t20 |
| OFF | t20 - t21 | 77.809 | 78 | 2136 | t21 |
| ON | t21 - t22 | 127.481 | 127 | 2263 | t22 |
| OFF | t22 - t23 | 67.794 | 68 | 2331 | t23 |
| ON | t23 - t24 | 136.950 | 137 | 2468 | t24 |
| OFF | t24 - t25 | 58.626 | 59 | 2527 | t25 |
| ON | t25 - t26 | 145.843 | 146 | 2673 | t26 |
| OFF | t26 - t27 | 49.967 | 50 | 2723 | t27 |
| ON | t27 - t28 | 154.056 | 154 | 2877 | t28 |
| OFF | t28 - t29 | 42.065 | 42 | 2919 | t29 |
| ON | t29 - t30 | 161.734 | 162 | 3081 | t30 |
| OFF | t30 - t31 | 34.665 | 35 | 3116 | t31 |
| ON | t31 - t32 | 168.779 | 169 | 3285 | t32 |
| OFF | t32 - t33 | 27.906 | 28 | 3313 | t33 |
| ON | t33 - t34 | 175.188 | 175 | 3488 | t34 |
| OFF | t34 - t35 | 21.854 | 22 | 3510 | t35 |
| ON | t35 - t36 | 180.974 | 181 | 3691 | t36 |
| OFF | t36 - t37 | 16.407 | 16 | 3707 | t37 |
| ON | t37 - t38 | 185.974 | 186 | 3893 | t38 |
| OFF | t38 - t39 | 11.760 | 12 | 3905 | t39 |
| ON | t39 -t40 | 190.107 | 190 | 4095 | t40 |
| OFF | t40 - t41 | 7.971 | 8 | 4103 | t41 |
| ON | t41 - t42 | 193.729 | 194 | 4297 | t42 |
| OFF | t42 - t43 | 4.724 | 5 | 4302 | t43 |
| ON | t43 - t44 | 196.314 | 196 | 4498 | t44 |
| OFF | t44 - t45 | 2.513 | 3 | 4501 | t45 |
| ON | t45 - t46 | 198.314 | 198 | 4699 | t46 |
| OFF | t46 - t47 | 0.896 | 1 | 4700 | t47 |
| ON | t47 - t48 | 199.305 | 200 | 4900 | t48 |
| OFF | t48 - t49 | 0.126 | 0 | 4900 | t49 |
| ON | t49 - t50 | 199.865 | 200 | 5100 | t50 |

We can observe that the time interval under 500 ns will be omitted. To achieve the control a strategy based on timer T2 proprieties was used. How the timer T2 may be read "on the fly", but not possesses extra read latches, the software must take into consideration this feature.

The idea of the control principle is to exploit the propriety of timer T2 to be used separately to set and reset the pins of the P4 port. When a long logic 1 is followed by a short logic 0 (even of 1 μs period) a interrupt routine based on CM0 compare register is used - CMI0 interruption flag. Consequently, when a 0 logic is followed by a short logic 1, a interrupt routine based on CM1 compare register is used - corresponding to CMI1 interruption flag. To switch the legs of the single-phase bridge an interrupt routine based on CM2 compare register (CMI2 interruption flag) is userd every 10,000 microseconds.

In the figure 1 is presented the structure of control system using 80C552 microcontroller. The switching devices are only generic presented, their specific problems being not the matter of study in our paper.

In the figure 2 is presented the principle of control based on switching the interrupt routines depending on the 1 logic and 0 logic time intervals. Also is explicit the principle of legs switching in the single-phase bridge. The critical time moments, correspondingly to the values in the Table 1 (when the interrupt type routine is changed) are mentioned.

In the figure 2 and in the following CMI0 interrupt routine is denoted by "INTSET', CMI1 interrupt routine is denoted by "INTRES" and CMI2 interrupt routine is identified by "INTTOG".

Figure 1. 80C552 pins assignment for the control system of PWM single-phase inverter

Figure 2. Waveforms for the control system. There are indicated the interruption routines used and associated time moments.

Taking into consideration the complexity of the waveforms in the figure 2, and the wide range of values for the switching times in the Table 1, only a powerful time control can achieve the features of control system. The timer T2 achieves these time control necessities. Its outlook allows the time control in sophisticated application such as engine management [3].

In the software, the switching times are placed in a table in the program memory area. The data is indexed addressed, using the register DPTR (Data Pointer) as 16 bits base register. Data readings are effected by appropriate interruption routine. How is presented in the figure 2, to load the appropriate time values in the compare registers (both CM0 and CM1), sometimes is used the CMI0 (INTSET) interrupt, sometimes CMI1 (INTRES). We have previously explained that is very important the registers loading order, and the match between the loading order and the use of a specific interruption routine.

For a better understanding of this principle, in the following the blocks of compare registers loading is presented for the two interrupt routines (INTSET and INTRES):

INTSET:	…

…

MOV A, CONTT

MOVC A,@A+DPTR

MOV CML1,A

INC CONTT

MOV A,CONTT

MOVC A,@A+DPTR

MOV CMH1,A

INC CONTT

MOV A,CONTT

MOVC A,@A+DPTR

MOV CML0,A

INC CONTT

MOV A,CONTT

MOVC A,@A+DPTR

MOV CMH0,A

…

RETI

We can observe that in the INTSET interrupt routine first is loaded the register CM1 (that reset the activated bits in port P4) and then the register CM0 (to set the activated bits in port P4).. In this way is possible to obtain very short pulses on 1 logic level (even 1 μs), despite relative long time necessary to load the compare registers.

INTRES:	…

…

MOV A, CONTT

MOVC A,@A+DPTR

MOV CML0,A

INC CONTT

MOV A,CONTT

MOVC A,@A+DPTR

MOV CMH0,A

INC CONTT

MOV A,CONTT

MOVC A,@A+DPTR

MOV CML1,A

INC CONTT

MOV A,CONTT

MOVC A,@A+DPTR

MOV CMH1,A

…

RETI

This time we can observe that in the INTRES interrupt routine first is loaded the register CM0 (that set the activated bits in port P4) and then the register CM1 (to reset the activated bits in port P4).. In this way is possible to obtain very short pulses on 0 logic level (even 1 μs).

CONTT is a software counter used in indexed with DPTR of the switching times table.

In the figure 3 the switching times table (TABTEM) and the way to access data using indexed addressing are presented. Also it results the interrupt routines management.

Figure 3. Switching times table: make-up, data destination and interrupt routines management

The counter CONTT is used in indexed addressing to select the appropriate data at a certain time and also to activate the adequate interrupt routine.

In the figure 2 could be observed the using of another interrupt routine denoted by INTTOG. This routine is activated every 10,000 μs (at the end of every semiperiod of 50 Hz waveform). When a match with CM2 occurs (at the event 10,000), the controller "toggles" bits 6 and 7 enabled using the corresponding bits of RTE. In this way the switching devices SW1 and SW2 (see figure 1) are controlled. It switches also the outputs P4.0 and P4.1 of port P4 to control the switching devices PWM1 and PWM2 (in the figure 1) on the correspondingly legs of the inverter bridge. This control is achieved via special function registers STE and RTE. Also this interrupt routine assures the reset of timer T2. When timer T2 reaches the state "10,000" the pin P4.2 of port P4 is set. The pin P4.2 is connected to the pin P1.5 (of the port P1) with alternative function RT2 - reset timer T2. A rising edge on the input signal RT2, if enabled, will reset the timer T2. To be possible this way of working must be set the control bit T2ER (timer T2 reset enable) in the special function register TM2CON. In the same special function register it was selected the prescaler to use the clock source = fosc / 12. After an adequate time period, the pin P4.2 is reset. In this way the timer T2 could be again reset after another period of 10,000 μs by a rising edge on the input RT2.

This approach makes possible to use the switching times table containing the values for a semiperiod (10,000 μs) to control the inverter for the whole period (20,000 μs).

# SUMMARY

We have tested and developed the software for the control system using an evaluation kit with Philips 80C552 microcontroller. It is easy to observe in the figure 1 that there are not necessary any additional hardware in the control system. Only a wire to connect reset timer T2 input (RT2) to the pin P4.2 of the port P4 to make possible the reset of timer T2 every 10,000 μs (every semiperiod) was used.

Using a crystal clock, the frequency stability reaches of course very high values.

Also it was effected a set of preliminary tests using power switching devices. These tests have confirmed the high quality of the control based on microcontroller techniques.

# REFERENCES

*** 80C51 Family Architecture, Philips Semiconductors, Philips Semiconductors, Sunnyvale, California, U.S.A., March 1995.

*** 80C51 Family Derivatives. 8XC552/562 overview, Philips Semiconductors, Sunnyvale, California, U.S.A., August 1996.

Metzermaekers D., Veldhuisen E. "Engine Management with PCB 83C552 Single-chip Microcontroller, PHILIPS, Electronic Components and Applications, vol. 9, no.1, 1989, pages 2-13.

# Text boxes

SW2

P4.7

SW1

P4.6

PWM2

P4.1

PWM1

P4.0

t0

PWM1

SW2

PWM2

SW1

RT2

PORT

P1

P1.5

PORT

P4

P4.7

P4.6

P4.5

P4.4

P4.3

P4.2

P4.1

P4.0

80C552

t49

t48

t47

t46

t77

t17

t0

t49

t48

t47

t46

t77

t17

0

INTSET

INTRES

INTRES

INTSET

INTRES

INTRES

INTTOG

INTTOG

CML0

20,000 μs

10,000 μs

1

2

CMH0

4

CMH1

3

CML1

8

CMH1

7

CML1

6

CMH0

5

CML0

36

CMH1

35

CML1

34

CMH0

33

CML0

32

CMH1

31

CML1

30

CMH0

29

CML0

38

CMH0

37

CML0

TABTM

(DPTR)

CONTT

160

CMH1

158

CML1

158

CMH0

157

CML0

156

CMH1

155

CML1

154

CMH0

153

CML0

152

CMH1

151

CML1

190

CMH0

189

CML0

188

CMH1

187

CML1

186

CMH0

185

CML0

INTRES

INTSET

INTRES

INTRES

t1

t2

t4

t3

t18

t17

t16

t15

t19

t80

t79

t78

t77

t76

t95

t94

t93

INTRES

RESET (CM1)

SET (CM0)

RESET (CM1)

SET (CM0)

RESET (CM1)

SET (CM0)

RESET (CM1)

SET (CM0)

SET (CM0)

RESET (CM1)

SET (CM0)

RESET (CM1)

SET (CM0)

RESET (CM1)

SET (CM0)

RESET (CM1)

SET (CM0)

INTRES

INTSET

INTSET

INTRES

INTSET

INTRES t0 - t17

INTSET t18 - t78

INTRES t79 - t95